## Slide 1: Fundamental Hydrogen-Air Mixing, Combustion and Particulate Formation Processes in H2ICE: Particle Formation in Hydrogen Combustion
Leonid Tartakovsky
Director, Internal Combustion Engines Laboratory
Technion – Israel Institute of Technology
Collaborators: Andy Thawko, Ben Holtzer, Arnon Poran, Amnon Eyal
ASME ICED Webinar Series: The Future of the Internal Combustion Engine
December 13, 2023

## Slide 2: Hydrogen is a Great Sustainable Fuel for IC Engine
2
Carbon-free
Wide flammability limits
High burning velocity (207 cm/s vs ~35 for gasoline)
Contributes to better antiknock performance
Wide-spread opinion:
Carbon-free hydrogen combustion in IC engine should lead to performance improvement and emissions reduction
Thawko et al., Energy Conversion & Management, 2022
Singh et al., Fuel, 2016

## Slide 3: Challenges of Hydrogen as an ICE Fuel
3
Because port reformate injection leads to abnormal combustion and power loss, we suggested employing the direct injection.
No fueling infrastructure available
Onboard storage is problematic
To remind: = 2.016 g/mol,
Boiling T = -253°C
Can be overcome through onboard on-demand hydrogen production

## Slide 4: Onboard on-demand Hydrogen Production From a Sustainable Fuel
Thermo-Chemical Recuperation (TCR)
Primary renewable low-carbon intensity liquid fuel (e-fuel)
Waste heat recovery process
Direct reformate injection
Hydrogen combustion
Ultra-low pollutant emissions
Methanol Steam Reforming (MSR)
CH3OH+H2O → 3H2+CO2 ΔH≈50 kJ/mol
Tartakovsky L., Sheintuch M., Veinblat M., Thawko A., International Patent Application No. PCT/IB2020/056382, 2021
Low reforming temperatures- 250-300 C
4
High-Pressure Thermo-Chemical Recuperation

## Slide 5: High-Pressure Thermo-Chemical Recuperation Performance
Chart: Engine Performance Improvement [%]
| Efficiency | CO | CO2 | HC | NOx
 | 18 | 90 | 10 | 85 | 73
MSR | 21 | 6 | 15 | 12 | 21
HP-TCR2 | 19 | 55 | 11 | 74 | 81
HP-TCR | 11 | 36 | 4 | 22 | 16
Chart: IMEP [bar]
| 1.4644615463272228 | 1.9568104669676321 | 2.9031294425193015 | 4.311781105950856 | 5.8372716848488269
Gasoline | 0.16152 | 0.19 | 0.22356 | 0.24923 | 0.23672
MSR 40 bar | 0.19379 | 0.274 | 0.30234 | 0.32621 | 0.33585 | 0.32403 | 0.27992 | 0.26281
MSR 50 bar | 0.33274
HP-TCR | 0.30853 | 0.31746 | 0.32343 | 0.32427 | 0.28885
19%-30% relative increase in indicated efficiency
A reduction in NOx, CO and HC emissions by up to 97, 91 and 96, respectively
Poran, Thawko et al., Int. J Hydrogen Energy, 2018
5

## Slide 6: Fuel Type Effect on Gaseous Pollutant Emission – DI Engine
CO is near-zero for MSR and hydrogen
CO2 for MSR - from the injected reformate
NOx is near-zero for MSR due to CO2
6

## Slide 7: Fuel Type Effect on DI Engine Performance
HP-TCR system efficiency is higher than for the pure hydrogen
Ultra-low NOx emission for the reformate due to CO2 presence
Ultra-low CO emission for both the reformate and hydrogen
Advanced EOI is favored because of better fuel-air mixing
Thawko et al., Energy Conversion and Management, 2022
7
HP-TCR system

## Slide 8: Total Particle Concentration Comparison
MSR
CH3OH+H2O → 3H2+CO2
Thawko et al., Int. J Hydrogen Energy, 2019
Previously Unknown Phenomenon
8
This result contradicts the previously published data and a straightforward intuition
Why?
Thawko et al., Energy Conversion and Management, 2022

## Slide 9: Particle Size Distribution – Different Oils
(a) Oil 1 (mineral)
(b) Oil 2 (synthetic)
Higher PN concentration for all particle size with the reformate
PM were collected and characterized- lubricant additives were found
Thawko et al., SAE Technical paper 2020-01-2200
9

## Slide 10: Particle Formation - Direct vs Port Fuel Injection
Single cylinder, Petter AD1 based | 
Bore x Stroke, mm | 80x73
Displacement, cm3 | 367
Compression ratio | 15-17.3
Power, kW @ speed, rpm | 5.3 @ 3000
Fuel injection system | Direct
 | Port
10
  Increased particles formation for direct injection
  Excessive lubricant involvement in the combustion

## Slide 11: Under-expanded Gaseous Jet Flow Field
Fundamental investigation at ICE typical conditions
Goal:
  Study of the transient underexpanded gaseous jet
  Detailed flow field characteristics
Method:
  Schlieren & PIV technique for the near- and far-field characterization, respectively
Thawko et al., Physics of Fluid, 2021
11

## Slide 12: Flow Field Characterization- Free Flow Jet
Vorticity
Swirling strength
Radial velocity
Axial velocity
Streamlines
  Air entrainment encouraged by the transient under expanded jet
I
II
Thawko et al., Physics of Fluid, 2021
12

## Slide 13: Flow Field Characterization- Impinging Jet
  Two rolled-up vortex regions with large-scale motion are formed in the wall jet region
  The lubricant vapor near cylinder walls entrained into the jet in the free-jet region and participates in the combustion
Vorticity
Swirling strength
13
Is this the main entrainment mechanism?

## Slide 14: Interaction of a Gaseous Impinging Jet with a Heated Lubricated Surface
  Perpendicular impinging jets were traced along the free, piston and liner jet regimes for further understanding of the entrainment mechanism
  The jets were injected onto heated piston and lubricated liner like surfaces to clarify the lubricant vapor entrainment phenomena
14
Several experiments were performed via Shadowgraph optical imaging Z-type configuration
Holtzer & Tartakovsky, SAE Technical Paper 2023-01-0308, 2023

## Slide 15: Main Lubricant Entrainment Mechanism
  Recirculation – entrainment of the lubricant vapor in the free-jet region
  Sweeping – entrainment of the lubricant vapor along the liner by the climbing roll-up
15
Holtzer & Tartakovsky, SAE Technical Paper 2023-01-0308, 2023
Sweeping is the main entrainment mechanism

## Slide 16: Particle Formation Mechanism in Non-premixed Combustion
Both for DI&PFI
Rogers et al. (2015)
Hydrogen low quenching distance
Excessive lubricant evaporation
Lubricant entrainment into combustion chamber bulk
Particle formation
16
Holtzer & Tartakovsky (2023)
Thawko & Tartakovsky, Fuel, 2022

## Slide 17: Particle Formation - Ignition Timing Effect
  Advanced ignition – increase in PN concentration
    Higher In-cylinder pressure followed by lower flame quenching distance
    More intensive lubricant evaporation
    More Lubricated surface exposed to flame
Thawko et al., Int. J Hydrogen Energy, 2019
Reformate fuel
17

## Slide 18: Non-premixed Combustion of Gaseous Fuel - Fuel Type Effect on Particle Emission
The fuel carbon content is the dominant influencing factor affecting particle formation at low loads
The lubricant becomes the dominant particle source with hydrogen-based fuel combustion
Reformate with the highest injection duration results in the highest particle formation
Particle Formation in a DI ICE
Flame Quenching Distance
Fuel Carbon Content
Injection Duration
18
Thawko et al., Energy Conversion and Management, 2022
Thawko & Tartakovsky, Fuel, 2022

## Slide 19: Summary
Excessive particle formation was discovered in reformate/hydrogen combustion compared to hydrocarbon fuels
Particle formation mechanism in non-remixed hydrogen combustion was described
Sweeping is the main lubricant vapor entrainment mechanism into the combustion chamber bulk
Longer injection duration results in a higher particle formation
The described particle formation mechanism paves the way to development of novel engineering solutions aimed at particle formation mitigation
19

## Slide 20: Acknowledgments
20

## Slide 21: Q & A
Thank you for your attention!
Prof. Leonid Tartakovsky
tartak@technion.ac.il
21